## Slide 1: Fluid Network Analysis
Saaketh Ramoju

## Slide 2: Goals
Develop an intuition for pressure and flow
Understand relationships between pressure and flow
Learn some of the basic math behind fluid network modeling
Apply conservation laws to solve a system
Differentiate between steady and transient solving methods
Discuss limitations with fluid properties
Explore some unique fluid phenomena

## Slide 3: Overview
Quick Warmup
Math Concepts
Solving Strategies
Fluid Properties
Fluid Systems
https://github.com/saakethramoju/Fluid-Network-Analysis-Lecture
So that you can follow along as I do the problems, I included a supplementary .mlx containing Matlab code
This code contains the problems I will discuss today

## Slide 4: Warmup

## Slide 5
Water
Water

## Slide 6: What is a fluid network & why should we care?
A fluid network is form of CFD, computational fluid dynamics
  It models system-level parameters
  Doesn’t model detailed flow phenomena
  A way to combine all your fluid math
Allows for quick iteration and system design without having to set up a costly and time-intensive CFD model of a large system
  Especially good when trying to work off of test data from rocket engines or prop systems

## Slide 7
Sea Level
Bottom of a 10ft pool

## Slide 8: Where does this apply?
How would we increase or decrease chamber pressure?
What if we fixed everything else and decreased Pc?

## Slide 9: Which branch has the highest current?

## Slide 10: Reapply the same concept
Is there another way to describe fluid resistance other than CdA?

## Slide 11: Numerical Methods

## Slide 12: Hardy Cross Method
Similar to Kirchoff’s, but resistances are flow-dependent and initially unknown
  around a loop
  at each node
Old-fashioned method, great for water/hydrualic networks
Good for doing hand calcs
Used by city planners and civil engineers
1
2
3
4
5
Pipe | L (ft) | d(in) | C
1 | 300 | 6 | 130
2 | 424 | 6 | 130
3 | 300 | 4 | 130
4 | 300 | 6 | 130
5 | 300 | 6 | 130

## Slide 13: Hardy Cross Method
Identify CCW loops and guess Q magnitude and direction in each line
Calculate head loss with Q assuming (head loss)
  Hazen-Williams (simpler for water): ,
  Darcy-Weisbach (general fluids, hard to find ): ,
Find the Q correction: , correct each Q.
Iterate until values are small.
Run the Hardy Cross code section to see it in action

## Slide 14: Hardy Cross Method
8
2
2
2
2
2.67
1.03
2.30
0.67
0.97

## Slide 15: Computerized Models
With computers, Hardy Cross is bad
  Computers allow for using normally tedious methods (Newton-Rhapson, Secant, Bisect, etc.)
Hardy Cross only works for steady flow, which is normally fine for simple water/hydraulic networks
  Transient models require timestepping
Computers can help model compressible flow, cavitation, valve actuations, temperatures, etc. (stuff you cant do by hand easily)
  GFSSP, ROCETs, Modelica, Simcenter Amesim

## Slide 16: How do we numerically find roots?
For simple functions, finding roots is easy (quadratic formula, Vieta's, etc.)
Have to use root finding methods for heavily nonlinear equations

## Slide 17: Newton's Method
Pick reasonable starting point
Find the derivative at that point
Find the root of the tangent
Find the new value of the function at that root
Repeat

## Slide 18: Newton’s Method
What if you have a system of equations?
Each equation is a function of multiple variables
Vector Function:

## Slide 19: Newton’s Method
You may have seen this before…
Jacobian matrix
It’s important to give a good first guess
Other method’s (e.g. bisect) only need a starting range
scipy is good Python package for these
  MATLAB has these built in
  (Please use python)

## Slide 20: Timestepping
Root solvers are best for steady-state
  You give an initial guess, boundary value problems
Most transient (unsteady) solvers are initial value problems
  You give starting values, not guesses
  The accuracy and ”stability” of time stepping methods really depends on the situation
  Again, use scipy

## Slide 21: Timestepping
Which method should we choose?
Forward Euler
Backward Euler
Runge-Kutta
Simple, but stable only for a few cases
Unconditionally stable, more computation power
Predictor-corrector method

## Slide 22: Differential-Algebraic Equations
Sometimes you want to enforce certain property while you iterate or timestep
  For example, you have PT data from a test and you want the pressure at a node match the pressure trace over time.
  You would need to decouple your pressure value from conservation equations and let it define the system
  You have to “trade” a variable to fix one
“Balance” such that
Make sure is actually dependent on or else this wont work

## Slide 23: Solving Methods

## Slide 24: Conservation Equations
For steady flow, what goes in, must come out
For unsteady (transient) flow, we can have buildup or drainage
What are the conservation equations we care about?
(Reynold’s Transport Theorem, Integral Form)

## Slide 25: Conservation Equations
How many equations will we need for each node?
For an incompressible “branch”, mass and momentum are used in conjunction to get mdot

## Slide 26: Steady State Flow
How do we “solve” the system?

## Slide 27: Steady State Flow
Define nodes and branches:
  Node: O-Dimensional control volume with a set mass and thermodynamic properties (u, h, P, T, etc.)
  Branch: 1-Dimensional control volume that carries flow properties as a state (, Q, etc.)
Steady State: properties are time-independent:
  We are solving for the set of node properties that the system will exhibit when it has no tendency to change due to internal or external forces

## Slide 28: Steady State Flow
Identify your nodes and the node properties you wish to solve for (usually will be pressure and something else)
Set up the residual equations for each node:
Set all residuals equal to zero and use a root solver to find the value of P and other variables that satisfy the system of equations
  Netwon’s Method, Bisect, etc.
  You will need to provide initial guesses or brackets for every independent variable

## Slide 29: Steady State Flow
Try to solve for the chamber pressure
Modify the Steady-State Chamber Pressure Section

## Slide 30: Steady State Flow
Steady flow will be the majority of models you make
  It tends to be more accurate, and you often don’t care about the transient behaviour
Things you can model with steady state
  TCA performance
  Required pressure ladders
  Choked flow
  Pump operation
  “If my tanks have this much pressure, how much thrust will I get?”

## Slide 31: Transient Flow
Unsteady flow requires that we account for the changing bulk value of each node.
  For this reason, nodes are assigned a volume corresponding to what they represent in real like (union fitting, TCA chamber, tank, etc.)
Instead of solving residual equations, the mass and internal energy of the nodes are stepped through time

## Slide 32: Transient Flow
Define your timestep and initial conditions
Identify your nodes and the node properties you wish to solve for (usually will be pressure and something else)
Set up the differential equations relating to mass conservation and energy conservation:
  ,
Lookup the state variables that give the new density and internal energy for each node

## Slide 33: Transient Flow
Very hard to do accurately, but it can be done
  Was used for SSME to model chill and engine startup transients, and it was pretty accurate
Things transient models could account for:
  Valve sequencing
  Fluid hammer
  Throttling (Open Ratio vs Cd curve needed)
  “When I open my valve, what does the mass flow look like over time?”
Transient models can be accurate, but there will always be phenomenon that are difficult to model or simply not worth modeling.
In this SSME model, for example, main chamber pressure deviates due to unpredictable preburner and turbopump behavior

## Slide 34: Fluid Properties

## Slide 35: What properties are needed?
State Postulate!
  Do you foresee any issues with trying to iterate pressure and temperature?

## Slide 36: Fluid Phases
In the vapor dome (saturated region), pressure and temperature are not independent.
  As phase change from liquid to gas, the pressure and temperature stay constant.
  A single pressure and temperature combination can yield multiple internal energies.
Iteration over temperature can also be numerically unstable due to the ratio of residual sizes
These issues are solved by iterating over P and h instead

## Slide 37: Mixtures
For every new component/species to a fluid mixture, a new degree of freedom is added (mass fraction: )
  Just two TD properties are no longer enough
  This also means just two conservation equations are not enough
Species conservation must also be introduced
  Assume that the fluid is non-reacting:
Not all mixtures are ideal gases!
  For real fluid mixtures, it’s not as simple are just taking weighted averages to find specific volume, enthalpy, etc.
Mixture modeling is usually one of the biggest hurdles for generalized fluid networks

## Slide 38: Fluid Lookups
Making a generalized fluid network means having access to digitalized fluid properties
  For steady state, lookups need to be able to give any properties with pressure enthalpy
  For transient, you may need lookups with density, entropy, etc.
CoolProp is great for purefluids, but not good for mixtures (including air)
  Coolprop also has a limited mixture database, mostly limited to binary mixtures
REFPROP is way better, but is harder to use and costs $325
NIST is handy for quick manual lookups
  BEWARE! Not all NIST chemicals share the same reference enthalpy, so do not blinding mix values without checking formation enthalpies
Cantera or Thermo are good if you want to define your own fluids, but otherwise they’re limited in Equation-of-State (EOS) capabilities
Getting RP-1 properties can be a challenge
  Use n-Dodecane in CoolProp/REFPROP
  Use RocketProps

## Slide 39: Fluid Lookups
Can be super annoying with solvers
Iterative solvers need freedom to try a wide range of points
  In-built solver often automatically calculate the partial derivatives in Jacobians by plugging in values a bunch of values and subtracting them
Online packages like CoolProp have limits to that available T and P ranges of fluid data, so the solver may throw errors
  SOLUTION 1: program the residual to be very high if P or T is outside the bounds
  SOLUTION 2: allow the solver to extrapolate values
REFPROP enforces data limits

## Slide 40: Fluid Systems

## Slide 41: Resistance
You have already seen mathematical relations for resistance:
  or
How much energy does a fluid need to expend to sustain a certain flowrate: , where
  This is usually a steady state property, it is independent of any time derivatives
  CAREFUL: The form we have here is referred to as pneumatic resistance, you may also see hydraulic resistance ()
Analogous to Ohm’s Law:
  Flow resistance is nonlinear
  Can easily do parallel/series flow calcs in the same way

## Slide 42: Resistance
Parallel Network
Relation to CdA
(NASA Definition)
Similar to the definition from earlier. Head is often proportional to or , so it’s helpful to redefine R

## Slide 43: Resistance
form ( accounts for units)
Incompressible Flow Coefficient:
Unchoked Swagelok Equation:
Choked Swagelok Equation:
Reader-Harris/Gallagher (for orifices):
  The compressible Swagelok equations and Reader-Harris Equations are equivalent to using the flow parameter
Other Familiar Forms

## Slide 44: Capacitance
Capacitance represents energy storage capability of a flow component:
  For a compressible fluid, energy can be stored in compression too
  Imagine an accumulator or a tank with an inlet and outlet
  This is a transient property, it depends on the time derivative of pressure
  This is analogous to an electrical capacitor, except this stores pressure instead of charge (
  Capacitance is accounted for in Node conservation
What’s the capacitance, C, of this fluid component?

## Slide 45: Capacitance

## Slide 46: Inertance
Represents the extra energy needed to accelerate a fluid from it’s current flowrate:
  This is a transient property of a flow branch
  Similar to an inductor (). For this reason, inertance is also referred to as inductance.
Restatement of Newton’s Second Law (unsteady Reynolds Transport):
   
  The inertia is the fluid’s mass, resisting the need to accelerate
  Density is variable for compressible flow
Again, this form is referred to as pneumatic inductance.
  Hydraulic inertance would be

## Slide 47: Pressure/Flow Sources
Pressure Sources:
  Provide a constant source of driving
  Magical tank that maintains the same head pressure
  Roughly what a centrifugal pump does, for a fixed downstream resistance
Flow sources
  Provide a constant source of Q or
  Roughly what a positive displacement pump does, assuming fixed downstream resistance

## Slide 48: Transient Mass Flow
Approximately how long does it take for the through this line to reach steady-state? (assuming )
  You may assume CdA remains constant
Forward Euler :
Fix the Transient Mass Flow Section in the code

## Slide 49: Transient Mass Flow
Roughly ~1.4 seconds!

## Slide 50: System Curves
Represent the head vs flowrate of an entire fluid system
  Usually for steady flow
  Usually these curves have to be determined experimentally
  This is what a pump curve is, just a for a single component
A balanced fluid network model can easily determine the resistances, inductances, and capacitances for every node an branch in your system, allowing you to extrapolate points on the system curve
Analogous to an RLC circuit
Different steady state system curves for varying resistance. Which one has the lowest resistance?

## Slide 51: Fluid Phenomena

## Slide 52: Fluid Hammer
When a fluid is brough to rest suddenly (usually through valve closure), the sudden accumulation of mass causes a pressure spike
  This spike oscillate through the system and can be modeled as a partial differential equation.
  This is a transient phenomenon
The peak magnitude of the spike can be modeled with the Joukowsky Equation:
  is the speed of sound in an incompressible fluid, which is given by (: Bulk Modulus)

## Slide 53: Combustion
Usually done as fixed volume process
Important to account for formation enthalpy and sensible enthalpy as bonds will break and reform

## Slide 54: Cavitating Flow
Sometimes flow can go so fast that its pressure drops below its saturation pressure
  It starts boiling, forming gas bubbles
This phenomenon is purposefully caused in a cavitating venturi to decouple the mass flow from downstream pressure
  Usually designed to have 15-20% for margin

## Slide 55: Thanks!