## Slide 1: TCA Project Part 1
Ryan Yuan

## Slide 2: Project Overview
Equilibrium Model
  Program a calculator to find the mole fractions, chamber temperature, and other critical values at chemical equilibrium
  MR = 2.0
TCA Contour
  Choose a MR and NFZ model
  Calculate performance variables
  Design a TCA contour
Design a TCA contour for an RP-1/LOX engine and calculate critical values

## Slide 3: Equilibrium Calculator

## Slide 4
MR = 2.0 -> ⦰ = 1.74
Python function(): iterate through T and minimize residual
T = 3404.6 K
Isentropic Flow Equations
Balance RP1-LOX combustion reaction
Solve system of 3 equations
Conservation of energy
Plug in enthalpies of formation
200 iterations
Workflow

## Slide 5: Mole Fractions
Species | CEA | CO H20 H2 | % Error | CO H2O CO2 | % Error | CO H2 CO2 | % Error | CO H2 OH | % Error
CO | 0.4167 | 0.4800 | +15.20% | NA | NA | 0.1084 | -73.98% | 0.4048 | -2.85%
H20 | 0.2684 | 0.3716 | +38.43% | NA | NA | ~ | ~ | ~ | ~
H2 | 0.1854 | 0.1484 | -19.94% | ~ | ~ | 0.5200 | 180.52% | 0.2818 | +52.02%
CO2 | 0.0765 | ~ | ~ | NA | NA | 0.3716 | 386% | ~ | ~
H | 0.0310 | ~ | ~ | ~ | ~ | ~ | ~ | ~ | ~
OH | 0.0192 | ~ | ~ | ~ | ~ | ~ | ~ | 0.3134 | +1529%

## Slide 6: Discussion
Why does the concentrations vary between your model and CEA?
  My model only uses 3 species while CEA accounts for all species
  The more major species I correctly choose, the more accurate my mole fractions are
    CO, H2O, and H2 most accurate, while CO, H2, and OH least accurate
How can you make your model more accurate?
  Use the Kp formula and water-gas shift reaction
    5 equations can now solve for 5 species
  Each species’ fractions become more accurate. The 5 major species make up 97.8% of the products concentration.
  Alternatively, write a program to minimize the Gibbs function G(T,p) to get all minor species

## Slide 7: Critical Values
Quantity | CEA | CO H20 H2 | % Err | CO H2O CO2 | % Err | CO H2 OH | % Err
Adiabatic Flame Temperature (K) | 3257 | 3405 | +4.53% | 3897 | +19.65% | 1254 | -61.51%
Chamber Molecular Weight (g/mol) | 20.67 | 20.44 | -1.11% | 20.44 | -1.12% | 17.23 | -16.64%
Chamber Specific Heat Ratio | 1.162 | 1.228 | +5.68% | 1.252 | +7.74% | 1.325 | +14.03%
Exhaust Mach Number | 2.777 | 2.779 | +0.07% | 2.791 | +0.50% | 2.832 | 1.98%
Exhaust Temperature (K) | 1669 | 1809 | +8.40% | 1968 | +17.91% | 545 | -67.34%
Exhaust Velocity (m/s) | 2594 | 2642 | +1.87% | 2793 | +7.69% | 1671 | -35.57%
Specific Impulse (s) | 264 | 269 | 1.71% | 284.8 | +7.69% | 170 | -35.72%

## Slide 8: Discussion
How much does your model vary from CEA and why?
  CO, H2O, and H2: low error of +0.07% (Me), high error of +8.40% (Te)
    Fairly accurate because uses the 3 major species of RP1-LOX reaction
What are the shortcomings of your model?
  Doesn’t use all species, so critical values will have noticeable error
What are some improvement techniques?
  Minimize Gibbs free energy to get all minor species for higher accuracy
How could you extend it to become a general equilibrium solver?
  Code is currently generalizable for any reaction with H, C, and O
  Account for other elements like N, which would add a fourth equation

## Slide 9: TCA Contour

## Slide 10
pyplot(x=MR, y=Isp)
pyplot(x=MR, y=Tc)
Verify Tc is reasonable
Calculate Cf and eps
Calculate performance variables
Select geometric variables
Workflow
Nozzle shape, chamber length, contraction ratio, etc.
NFZ model
Find MR to maximize Isp

## Slide 11: MR = 2.4
Maximize Isp
Ensure Tc at that MR is not too hot for the engine
NFZ Model = 2
NFZ = 2: Assume equilibrium in chamber and frozen at throat
Chamber: the reaction happens so fast that it’s always in equilibrium, meaning net reaction rate = 0
Throat: the expansion happens so fast that the reaction essentially “freezes”, meaning mole fractions stays fixed
This is the most accurate assumption, balanced between equilibrium flow (higher Isp), and frozen flow (lower Isp)

## Slide 12: MR = 2.4

## Slide 13: Performance Variables
Design Variable | Value | Calculation
Mixture Ratio | 2.4 | f(Isp, Tc)
Performance Variables | Value | Calculation
Specific Impulse (s) | 258 | f(MR)
Chamber Temperature (K) | 3466 | f(MR)
Ideal Thrust Coefficient | 1.50 | cea(MR, Pc, Pamb, e)
Actual Thrust Coefficient | 1.42 | cea(MR, Pc, Pamb, e)
Performance Variable | Value | Calculation
Ideal C* (m/s) | 1782 | 
Actual C* (m/s) | 1640 | 
Ideal Exit Velocity (m/s) | 2677 | 
Actual Exit Velocity (m/s) | 2329 | 
Total Mass Flow (kg/s) | 4.76 | 
LOX Mass Flow (kg/s) | 3.36 | 
RP1 Mass Flow (kg/s) | 1.40 | 
Performance Variable | Value | Calculation
Ideal C* (m/s) | 1782 | 
Actual C* (m/s) | 1640 | 
Ideal Exit Velocity (m/s) | 2677 | 
Actual Exit Velocity (m/s) | 2329 | 
Total Mass Flow (kg/s) | 4.76 | 
LOX Mass Flow (kg/s) | 3.36 | 
RP1 Mass Flow (kg/s) | 1.40 | 

## Slide 14: Discussion
Specific Impulse (s)
  How efficient the engine is
  Higher Isp = more Δv for the same propellant mass
  Factors in optimizing Isp
    Propellant choice, MR
Characteristic Velocity (m/s)
  Quality of combustion in the chamber
  Factors in optimizing C*
    Injector design, chamber length
Thrust Coefficient
  How effectively the nozzle converts Pc to thrust
  Factors in optimizing Cf
    Eps: balance between underexpanded and overexpanded

## Slide 15: Geometric Variables
Geometric Variable | Value | Calculation
Throat Area (in^2) | 5.869 | 
Throat Radius (in) | 1.367 | 
Expansion Ratio | 5.3 | cea(Cf, Pe, Pc, Pamb, MR)
Geometric Variable | Value | Calculation
Throat Area (in^2) | 5.869 | 
Throat Radius (in) | 1.367 | 
Expansion Ratio | 5.3 | cea(Cf, Pe, Pc, Pamb, MR)
Geometric Variable | Value | Range
Nozzle Shape | Bell | N/A
Chamber Cylindrical Length (in) | 8.5 | N/A
Contraction Ratio | 3.5 | 3-4
Convergence Half-Angle (°) | 37.5 | 35-40
Convergence Radius (Rc/Rt) | 1.25 | 1.0-1.5
Lead-in Radius (Rtc/Rt) | 1.5 | 1.5
Divergence Half-Angle (°) | 15 | 12-18
Divergence Entrance Angle (°) | 30 | 30-32
Divergence Exit Angle (°) | 8 | 8-9
Percent Bell Lf (%) | 70 | 60-80

## Slide 16: TCA Contour

## Slide 17: Next Steps
TCA Part 2
CFD Analysis
Fullscale Engine Dev project🙏

## Slide 18: Thanks for Listening